## Slide 1: Mainia Mainship 390 #350
AC Wiring Diagram
Modification for
Freedom Marine 25 Inverter/Charger
Boat Departure Checklist – Shore Powered
>Link 2000: Inverter “OFF”, Batt Charger “ON”, “AC” on light green.
Boat Departure Checklist – Off Grid/Anchored
>Link 2000: Inverter “OFF”. 12V Refrigerator Switch (RH Column) “ON”

## Slide 2: Open Questions
30A Water Heater Main Panel Switch
40A N.O. Contactor Relay – LOAD side
Freedom AC 2 Out
40A N.O. Contactor Relay – control side
Water Heater
Freedom AC 1 IN
Option? : add contactor relay to open water heater circuit except when Freedom AC 1 In is hot to ensure water can’t be heated using inverter power

## Slide 3
Basic Information / Notes
Shore Power supply “AC 1” and “AC 2” details not shown on diagrams:
  Shore cords can be attached to inlets at the bow OR stern.
  30A breakers, located at each inlet, provide downstream overload protection.
  The inlets feed the main panel through two pairs of dual-pole, break-before-make switches. Each switch pair can connect “off, “fwd” OR “aft”, but not both.
Main Panel source selector switch pairs labeled “A” and “B” in diagrams:
  Switch pairs “A” and “B” are two 30A dual-pole breakers. Each pair is interlocked to break-before-make, and permit “both-off” OR “one-on”, but not “both-on”.
  Switch pair “A” selects either “AC 1 Shore” OR “Generator” to feed to Main Panel side 1. Switch pair “B” selects the feed to Main Panel side 2 by either paralleling with side one, OR from “AC 2” shore power.

## Slide 4
Basic Information / Notes (cont’d)
Freedom Marine 25 Inverter/Charger operational details:
  Contains an automatic, internal “transfer switch”. The inverter is “OFF” when “AC 1 IN” or “AC 2 IN” are supplied power.
  The Freedom 25 output is protected by an integral, manually reset, 30A breaker.
  The Freedom’s inverter will automatically supply up to 2.5KVA when no AC is supplied. Note: the inverter can be switched “off” using the Link 2000 mounted fwd of the main electrical panel.
  “AC 1 IN” powers “AC 1 OUT” and the battery charger.
  When power is supplied via “AC 1 IN” the Charger provides up to 130A of battery charging. The charger does not operate from “AC 2 IN”.
  “AC 1 IN” supplies power to “AC 2 OUT”, except if “AC 2 IN” is supplied power, in which case “AC 2 IN” supplies “AC 2 OUT”. This is represented in the small block diagram on each page.
  The Freedom 25 has a “Power Share” feature that will try to limit the total load on “AC 1 IN” to 30A max. by automatically reducing the battery charger’s power demand as needed.

## Slide 5
Freedom Internal AC 1 to AC 2 Switch Closed
AC 2 out = AC 1 in
Freedom
AC 1 Side
(Charger)
Boat AC 1 Side
8kw Generator
15A Breaker
15A Breaker
30A Breaker
Boat AC 2 Side
Aux (legacy) Battery Charger
30A Water Heater
15A Breaker
Shore Cord 1
Pair “A”
(See Note)
Freedom
AC 2 Side
(AC 1, or AC 2 pass thru)
Shore 1 Only, feeds Side 2 thru Freedom – BEST Dockside Setup
Best: Automatically PARALLELS “AC 1 IN” to Main Panel Side 2 through the Freedom’s internal transfer switch. The Freedom’s Power-Share feature can see the whole load and will adjust the battery charger demand to try to limit the total load on Shore 1 to 30A max.
Shore Cord 2 not connected
CHARGER
(on)
INVERTER
(off)
AC in 1
AC out 2
AC in 2
AC out 1
AC#1
AC#1
AC#2
AC#1
B
(See Note)
< Shore 1 On
< Gen OFF
Shore 2 On or Off >
Parallel Off >

## Slide 6
Freedom
AC 1 Side
(Charger)
Boat AC 1 Side
30A Breaker
30A Breaker
30A Breaker
Boat AC 2 Side
Aux Battery Charger
Water Heater
30A Breaker
Shore Cord 1
B
A
Freedom
AC 2 Side
(AC 1, or AC 2 pass thru)
Shore Cord 2
Freedom Internal AC 1 to AC 2 Switch Open
AC 2 out = AC 1 in
Shore 1 Paralleled to Side 2 B4 Freedom (but: see note below)
Ok, but not as good as “shore 1 only”: the Freedom’s Power Sharer feature doesn’t see the Shore 1 load paralleled direct to side 2, and can’t adjust the battery charger demand for the side 2 usage. Total load on Shore 1 side could exceed 30A, tripping a breaker (similar to legacy config. w/o Freedom).
8kw Generator
CHARGER
(on)
INVERTER
(off)
AC in 1
AC out 2
AC in 2
AC out 1
AC#1
AC#1
AC#2
AC#1
< Shore 1 On
< Gen OFF
< Parallel On
< Shore 2 Off

## Slide 7
Freedom
AC 1 Side
(Charger)
8kw Generator
Boat AC 1 Side
30A Breaker
30A Breaker
30A Breaker
Boat AC 2 Side
Aux Battery Charger
Water Heater
30A Breaker
Shore Cord 1
B
A
Freedom
AC 2 Side
(AC 1, or AC 2 pass thru)
Shore Cord 2
Shore 1 and Shore 2 – Fine if two 30A dock cord/supplies available
Freedom Internal AC 1 to AC 2 Switch Open
AC 2 out = AC 2 in
CHARGER
(on)
INVERTER
(off)
AC in 1
AC out 2
AC in 2
AC out 1
AC#1
AC#1
AC#2
AC#2
< Shore 1 On
< Gen OFF
Shore 2 On >
Parallel Off >

## Slide 8
Freedom
AC 1 Side
(Charger)
Boat AC 1 Side
8kw Generator
30A Breaker
30A Breaker
30A Breaker
Boat AC 2 Side
Aux Battery Charger
Water Heater
30A Breaker
Shore Cord 1 not connected
B
A
Freedom
AC 2 Side
(AC 1, or AC 2 pass thru)
Shore Cord 2
Shore 2 Only – Not Usual, but not hazardous
Freedom Internal AC 1 to AC 2 Switch Open
No AC 1 out
AC 2 out = AC 2 in
CHARGER
(off)
INVERTER
(off)
AC in 1
AC out 2
AC in 2
AC out 1
AC#1
AC#1
AC#2
AC#2
Shore 1 On or Off >
< Gen OFF
Shore 2 On >
Parallel Off >

## Slide 9
Freedom
AC 1 Side
(Charger)
Boat AC 1 Side
8kw Generator
30A Breaker
30A Breaker
30A Breaker
Boat AC 2 Side
Aux Battery Charger
Water Heater
30A Breaker
Shore Cord 1
B
A
Freedom
AC 2 Side
(AC 1, or AC 2 pass thru)
Shore Cord 2 not connected
Generator paralleled through the Inverter
Internal Freedom AC 1 to AC 2 Switch Open
AC 2 out = AC 1 in
Good Generator Load Management – But limited to 30A max .
Power Share feature sees whole load, adjusts battery charger load to try to limit the total generator load to 30A. Over 30A total load may trip a breaker.
CHARGER
(on)
INVERTER
(off)
AC in 1
AC out 2
AC in 2
AC out 1
AC#1
AC#1
AC#2
AC#1
Shore 1 Off >
Gen On >
Shore 2 On or Off >
Parallel Off >

## Slide 10
Freedom
AC 1 Side
(Charger)
Boat AC 1 Side
8kw Generator
30A Breaker
30A Breaker
30A Breaker
Boat AC 2 Side
Aux Battery Charger
Water Heater
30A Breaker
Shore Cord 1
B
A
Freedom
AC 2 Side
(AC 1, or AC 2 pass thru)
Shore Cord 2
Generator Paralleled before Freedom
Internal Freedom AC 1 to AC 2 Switch Open
AC 2 out = AC 1 in
CHARGER
(on)
INVERTER
(off)
AC in 1
AC out 2
AC in 2
AC out 1
GEN
GEN
GEN
GEN
Permits Max Generator Output and Provides Partial Generator Load Management by Power-Share feature on side 1.

## Slide 11
Freedom
AC 1 Side
(Charger)
Boat AC 1 Side
8kw Generator
30A Breaker
30A Breaker
30A Breaker
Boat AC 2 Side
Aux Battery Charger
Water Heater
30A Breaker
Shore Cord 1
B
A
Freedom
AC 2 Side
(AC 1, or AC 2 pass thru)
Shore Cord 2
No External Supply – Inverter Operating
Internal Freedom AC 1 to AC 2 Switch Closed
AC 2 out = AC 1 in
CHARGER
(off)
INVERTER
(on)
AC in 1
AC out 2
AC in 2
AC out 1
AC#1
INVRT
AC#2
INVRT
Inverter Power for House Loads - limited to 30A max .
WATER HEATER AND AUX BATTERY CHARGER MUST BE SWITCHED OFF WHEN on INVERTER POWER